## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Chapter 2
© 2008 Pearson Education

## Slide 2
The position of each digit in a weighted number system is assigned a weight based on the base or radix of the system. The radix of decimal numbers is ten, and only ten symbols (0 through 9) are used to represent any number.
Chapter 2
The column weights of decimal numbers are powers of ten that increase from right to left beginning with 100 =1:
Decimal Numbers
…105 104 103 102 101 100.
For fractional decimal numbers, the column weights are negative powers of ten that decrease from left to right:
102 101 100. 10-1 10-2 10-3 10-4 …

## Slide 3
Chapter 2
Decimal Numbers
Express the number 480.52 as the sum of values of each digit.
Example
Solution
(9 x 103) + (2 x 102) + (4 x 101) + (0 x 100)
or
9 x 1000 + 2 x 100 + 4 x 10 + 0 x 1
Decimal numbers can be expressed as the sum of the products of each digit times the column value for that digit. Thus, the number 9240 can be expressed as
480.52 = (4 x 102) + (8 x 101) + (0 x 100) + (5 x 10-1) +(2 x 10-2)

## Slide 4
Chapter 2
Binary Numbers
For digital systems, the binary number system is used. Binary has a radix of two and uses the digits 0 and 1 to represent quantities.
The column weights of binary numbers are powers of two that increase from right to left beginning with 20 =1:
…25 24 23 22 21 20.
For fractional binary numbers, the column weights are negative powers of two that decrease from left to right:
22 21 20. 2-1 2-2 2-3 2-4 …

## Slide 5
Chapter 2
Binary Numbers
A binary counting sequence for numbers from zero to fifteen is shown.
0 0 0 0 0
1 0 0 0 1
2 0 0 1 0
3 0 0 1 1
4 0 1 0 0
5 0 1 0 1
6 0 1 1 0
7 0 1 1 1
8 1 0 0 0
9 1 0 0 1
10 1 0 1 0
11 1 0 1 1
12 1 1 0 0
13 1 1 0 1
14 1 1 1 0
15 1 1 1 1
Decimal Number
Binary Number
Notice the pattern of zeros and ones in each column.
Digital counters frequently have this same pattern of digits:

## Slide 6
Chapter 2
Binary Conversions
The decimal equivalent of a binary number can be determined by adding the column values of all of the bits that are 1 and discarding all of the bits that are 0.
Convert the binary number 100101 to decimal.
Example
Solution
Start by writing the column weights; then add the weights that correspond to each 1 in the number.
25 24 23 22 21 20
32 16 8 4 2 1
1 0 0 1 0 1
32 +0 +0 +4 +0+1 =
37

## Slide 7
Chapter 2
Binary Conversions
You can convert a decimal whole number to binary by reversing the procedure. Write the decimal weight of each column and place 1’s in the columns that sum to the decimal number.
Convert the decimal number 49 to binary.
Example
Solution
The column weights double in each position to the right. Write down column weights until the last number is larger than the one you want to convert.
26 25 24 23 22 21 20.
64 32 16 8 4 2 1.
0 1 1 0 0 0 1.

## Slide 8
Chapter 2
You can convert a decimal fraction to binary by repeatedly multiplying the fractional results of successive multiplications by 2. The carries form the binary number.
Convert the decimal fraction 0.188 to binary by repeatedly multiplying the fractional results by 2.
Example
Solution
0.188 x 2 = 0.376 carry = 0
0.376 x 2 = 0.752 carry = 0
0.752 x 2 = 1.504 carry = 1
0.504 x 2 = 1.008 carry = 1
0.008 x 2 = 0.016 carry = 0
Answer = .00110 (for five significant digits)
MSB
Binary Conversions

## Slide 9
1
0
0
1
1
0
Chapter 2
You can convert decimal to any other base by repeatedly dividing by the base. For binary, repeatedly divide by 2:
Convert the decimal number 49 to binary by repeatedly dividing by 2.
Example
Solution
You can do this by “reverse division” and the answer will read from left to right. Put quotients to the left and remainders on top.
49 2
Decimal number
base
24
remainder
Quotient
12
6
3
1
0
Continue until the last quotient is 0
Answer:
Binary Conversions

## Slide 10
Chapter 2
Binary Addition
The rules for binary addition are
0 + 0 = 0 Sum = 0, carry = 0
0 + 1 = 1 Sum = 1, carry = 0
1 + 0 = 1 Sum = 1, carry = 0
1 + 1 = 10 Sum = 0, carry = 1
When an input carry = 1 due to a previous result, the rules are
1 + 0 + 0 = 01 Sum = 1, carry = 0
1 + 0 + 1 = 10 Sum = 0, carry = 1
1 + 1 + 0 = 10 Sum = 0, carry = 1
1 + 1 + 1 = 11 Sum = 1, carry = 1

## Slide 11
Chapter 2
Binary Addition
Add the binary numbers 00111 and 10101 and show the equivalent decimal addition.
Example
Solution
00111 7
10101 21
0
1
0
1
1
1
1
0
1
28
=
1 + 0 + 0 = 01 Sum = 1, carry = 0
1 + 0 + 1 = 10 Sum = 0, carry = 1
1 + 1 + 0 = 10 Sum = 0, carry = 1
1 + 1 + 1 = 11 Sum = 1, carry = 1
Rules

## Slide 12
Chapter 2
Binary Subtraction
The rules for binary subtraction are
0 - 0 = 0
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1 with a borrow of 1
Subtract the binary number 00111 from 10101 and show the equivalent decimal subtraction.
Example
Solution
00111 7
10101 21
0
/1
1
1
1
0
14
/1
/1
=

## Slide 13
Chapter 2
1’s Complement
The 1’s complement of a binary number is just the inverse of the digits. To form the 1’s complement, change all 0’s to 1’s and all 1’s to 0’s.
For example, the 1’s complement of 11001010 is
00110101
In digital circuits, the 1’s complement is formed by using inverters:
1 1 0 0 1 0 1 0
0 0 1 1 0 1 0 1

## Slide 14
Chapter 2
2’s Complement
The 2’s complement of a binary number is found by adding 1 to the LSB of the 1’s complement.
Recall that the 1’s complement of 11001010 is
00110101 (1’s complement)
To form the 2’s complement, add 1:
+1
00110110 (2’s complement)
1 1 0 0 1 0 1 0
0 0 1 1 0 1 0 1
1
0 0 1 1 0 1 1 0

## Slide 15
Chapter 2
Signed Binary Numbers
Signed numbers can be represented in three forms:
Sign-magnitude
1’s Complement
2’s Complement
In all cases, the MSB in a signed number is the sign bit, that
tells you if the number is positive or negative.
In all cases the positive number is represented in the same way.

## Slide 16
Chapter 2
Sign-magnitude Representation
In sign-magnitude the MSB represents the sign and rest of the bits represent the magnitude
For example +25 in sign-magnitude form is represented as:
00011001
Sign bit
Magnitude bits
And -25 in sign-magnitude form will be represented as:
10011001
Sign bit
Magnitude bits

## Slide 17
Chapter 2
1’s Complement Representation
Positive numbers in 1’s complement are represented in the same way as in sign-magnitude form:
For example +25 in 1’s complement form is represented as:
00011001 (as before)
And -25 in 1’s complement form is represented in one’s complement of the corresponding positive representation:
11100110

## Slide 18
Chapter 2
2’s Complement Representation
Positive numbers in 2’s complement are represented in the same way as in sign-magnitude and 1’s complement forms:
For example +25 in 2’s complement form is represented as:
00011001 (as before)
And -25 in 2’s complement form is represented in two’s complement of the corresponding 1’s complement:
11100110 + 1 = 11100111
1’s complement
Add 1
2’s complement

## Slide 19
Chapter 2
Finally, therefore
Decimal Number | Sign-magnitude | 1’s Complement | 2’s Complement
+25 | 00011001 | 00011001 | 00011001
- 25 | 10011001 | 11100110 | 11100111
Least used
Most popular

## Slide 20
Chapter 2
Arithmetic Operations with Signed Numbers
Using the signed number notation with negative numbers in 2’s complement form simplifies addition and subtraction of signed numbers.
Rules for addition: Add the two signed numbers. Discard any final carries. The result is in signed form.
Examples:
00011110 = +30
00001111 = +15
00101101
= +45
00001110 = +14
11101111 = -17
11111101
= -3
11111111 = -1
11111000 = -8
11110111
= -9
1
Discard carry

## Slide 21
Chapter 2
Arithmetic Operations with Signed Numbers
01000000 = +128
01000001 = +129
10000001
= -126
10000001 = -127
10000001 = -127
100000010
= +2
Note that if the number of bits required for the answer is exceeded, overflow will occur. This occurs only if both numbers have the same sign. The overflow will be indicated by an incorrect sign bit.
Two examples are:
Wrong! The answer is incorrect and the sign bit has changed.
Discard carry

## Slide 22
Chapter 2
Arithmetic Operations with Signed Numbers
Rules for subtraction: 2’s complement the subtrahend and add the numbers. Discard any final carries. The result is in signed form.
00001111
= +15
1
Discard carry
2’s complement subtrahend and add:
00011110 = +30
11110001 = -15
Repeat the examples done previously, but subtract:
00011110
00001111
-
00001110
11101111
11111111
11111000
-
-
00011111
= +31
00001110 = +14
00010001 = +17
00000111
= +7
1
Discard carry
11111111 = -1
00001000 = +8
(+30)
–(+15)
(+14)
–(-17)
(-1)
–(-8)

## Slide 23
Chapter 2
Hexadecimal Numbers
Hexadecimal uses sixteen characters to represent numbers: the numbers 0 through 9 and the alphabetic characters A through F.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 8 9 A B C D E F
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Hexadecimal
Binary
Large binary number can easily be converted to hexadecimal by grouping bits 4 at a time and writing the equivalent hexadecimal character.
Express 1001 0110 0000 11102 in hexadecimal:
Example
Solution
Group the binary number by 4-bits starting from the right. Thus, 960E

## Slide 24
Chapter 2
Hexadecimal Numbers
Hexadecimal is a weighted number system. The column weights are powers of 16, which increase from right to left.
.
1 A 2 F16
670310
Column weights
163 162 161 160
4096 256 16 1
.
{
Express 1A2F16 in decimal.
Example
Solution
Start by writing the column weights:
4096 256 16 1
1(4096) + 10(256) +2(16) +15(1) =
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 8 9 A B C D E F
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Hexadecimal
Binary

## Slide 25
Chapter 2
Octal Numbers
Octal uses eight characters the numbers 0 through 7 to represent numbers. There is no 8 or 9 character in octal.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 10 1112 13 14 15 16 17
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Octal
Binary
Binary number can easily be converted to octal by grouping bits 3 at a time and writing the equivalent octal character for each group.
Express 1 001 011 000 001 1102 in octal:
Example
Solution
Group the binary number by 3-bits starting from the right. Thus, 1130168

## Slide 26
Chapter 2
Octal Numbers
Octal is also a weighted number system. The column weights are powers of 8, which increase from right to left.
.
3 7 0 28
198610
Column weights
83 82 81 80
512 64 8 1
.
{
Express 37028 in decimal.
Example
Solution
Start by writing the column weights:
512 64 8 1
3(512) + 7(64) +0(8) +2(1) =
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 10 1112 13 14 15 16 17
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Octal
Binary

## Slide 27
Chapter 2
BCD
Binary coded decimal (BCD) is a weighted code that is commonly used in digital systems when it is necessary to show decimal numbers such as in clock displays.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Binary
BCD
0001 0001 0001 0001 0001 0001
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 0000 0001 0010 0011 0100 0101
The table illustrates the difference between straight binary and BCD. BCD represents each decimal digit with a 4-bit code. Notice that the codes 1010 through 1111 are not used in BCD.

## Slide 28
Chapter 2
BCD
You can think of BCD in terms of column weights in groups of four bits. For an 8-bit BCD number, the column weights are: 80 40 20 10 8 4 2 1.
Question:
What are the column weights for the BCD number 1000 0011 0101 1001?
Answer:
8000 4000 2000 1000 800 400 200 100 80 40 20 10 8 4 2 1
Note that you could add the column weights where there is a 1 to obtain the decimal number. For this case:
8000 + 200 +100 + 40 + 10 + 8 +1 = 835910

## Slide 29
Chapter 2
BCD
A lab experiment in which BCD is converted to decimal is shown.

## Slide 30
Chapter 2
Gray code
Gray code is an unweighted code that has a single bit change between one code word and the next in a sequence. Gray code is used to avoid problems in systems where an error can occur if more than one bit changes at a time.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Binary
Gray code
0000 0001 0011 0010 0110 0111 0101 0100 1100 1101 1111 1110 1010 1011 1001 1000

## Slide 31
Chapter 2
Binary  Gray code
Binary sequence
Gray code sequence

## Slide 32
Chapter 2
Gray code  Binary
Gray code sequence
Binary sequence

## Slide 33
Chapter 2
Gray code
A shaft encoder is a typical application. Three IR emitter/detectors are used to encode the position of the shaft. The encoder on the left uses binary and can have three bits change together, creating a potential error. The encoder on the right uses gray code and only 1-bit changes, eliminating potential errors.
Binary sequence
Gray code sequence

## Slide 34
Chapter 2
ASCII
ASCII is a code for alphanumeric characters and control characters. In its original form, ASCII encoded 128 characters and symbols using 7-bits. The first 32 characters are control characters, that are based on obsolete teletype requirements, so these characters are generally assigned to other functions in modern usage.
In 1981, IBM introduced extended ASCII, which is an 8-bit code and increased the character set to 256. Other extended sets (such as Unicode) have been introduced to handle characters in languages other than English.

## Slide 35
Chapter 2
Parity Method
The parity method is a method of error detection for simple transmission errors involving one bit (or an odd number of bits). A parity bit is an “extra” bit attached to a group of bits to force the number of 1’s to be either even (even parity) or odd (odd parity).
The ASCII character for “a” is 1100001 and for “A” is 1000001. What is the correct bit to append to make both of these have odd parity?
Example
Solution
The ASCII “a” has an odd number of bits that are equal to 1; therefore the parity bit is 0. The ASCII “A” has an even number of bits that are equal to 1; therefore the parity bit is 1.

## Slide 36
Chapter 2
Cyclic Redundancy Check
The cyclic redundancy check (CRC) is an error detection method that can detect multiple errors in larger blocks of data. At the sending end, a checksum is appended to a block of data. At the receiving end, the check sum is generated and compared to the sent checksum. If the check sums are the same, no error is detected.

## Slide 37
Selected Key Terms
Byte
Floating-point number
Hexadecimal
Octal
BCD
A group of eight bits
A number representation based on scientific notation in which the number consists of an exponent and a mantissa.
A number system with a base of 16.
A number system with a base of 8.
Binary coded decimal; a digital code in which each of the decimal digits, 0 through 9, is represented by a group of four bits.

## Slide 38
Selected Key Terms
Alphanumeric
ASCII
Parity
Cyclic redundancy check (CRC)
Consisting of numerals, letters, and other characters
American Standard Code for Information Interchange; the most widely used alphanumeric code.
In relation to binary codes, the condition of evenness or oddness in the number of 1s in a code group.
A type of error detection code.

## Slide 39
1. For the binary number 1000, the weight of the column with the 1 is
a. 4
b. 6
c. 8
d. 10
© 2008 Pearson Education
Quiz

## Slide 40
2. The 2’s complement of 1000 is
a. 0111
b. 1000
c. 1001
d. 1010
© 2008 Pearson Education
Quiz

## Slide 41
3. The fractional binary number 0.11 has a decimal value of
a. ¼
b. ½
c. ¾
d. none of the above
© 2008 Pearson Education
Quiz

## Slide 42
4. The hexadecimal number 2C has a decimal equivalent value of
a. 14
b. 44
c. 64
d. none of the above
© 2008 Pearson Education
Quiz

## Slide 43
5. Assume that a floating point number is represented in binary. If the sign bit is 1, the
a. number is negative
b. number is positive
c. exponent is negative
d. exponent is positive
© 2008 Pearson Education
Quiz

## Slide 44
6. When two positive signed numbers are added, the result may be larger that the size of the original numbers, creating overflow. This condition is indicated by
a. a change in the sign bit
b. a carry out of the sign position
c. a zero result
d. smoke
© 2008 Pearson Education
Quiz

## Slide 45
7. The number 1010 in BCD is
a. equal to decimal eight
b. equal to decimal ten
c. equal to decimal twelve
d. invalid
© 2008 Pearson Education
Quiz

## Slide 46
8. An example of an unweighted code is
a. binary
b. decimal
c. BCD
d. Gray code
© 2008 Pearson Education
Quiz

## Slide 47
9. An example of an alphanumeric code is
a. hexadecimal
b. ASCII
c. BCD
d. CRC
© 2008 Pearson Education
Quiz

## Slide 48
10. An example of an error detection method for transmitted data is the
a. parity check
b. CRC
c. both of the above
d. none of the above
© 2008 Pearson Education
Quiz

## Slide 49
Answers:
1. c
2. b
3. c
4. b
5. a
6. a
7. d
8. d
9. b
10. c
Quiz