## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Chapter 3
© 2008 Pearson Education

## Slide 2
The inverter performs the Boolean NOT operation. When the input is LOW, the output is HIGH; when the input is HIGH, the output is LOW.
Summary
The Inverter
A
X
LOW (0) HIGH (1)
HIGH (1) LOW(0)
The NOT operation (complement) is shown with an overbar. Thus, the Boolean expression for an inverter is X = A.

## Slide 3
Summary
The Inverter
Example waveforms:
A
X
A
X
A group of inverters can be used to form the 1’s complement of a binary number:
Binary number
1’s complement
1 0 0 0 1 1 0 1
0 1 1 1 0 0 1 0

## Slide 4
The AND gate produces a HIGH output when all inputs are HIGH; otherwise, the output is LOW. For a 2-input gate, the truth table is
Summary
The AND Gate
The AND operation is usually shown with a dot between the variables but it may be implied (no dot). Thus, the AND operation is written as X = A .B or X = AB.
0 0
0 1
1 0
1 1
0
0
0
1
A
B
X
A
B
X

## Slide 5
Summary
Example waveforms:
A
X
The AND operation is used in computer programming as a selective mask. If you want to retain certain bits of a binary number but reset the other bits to 0, you could set a mask with 1’s in the position of the retained bits.
The AND Gate
A
B
X
B
00000011
Example
If the binary number 10100011 is ANDed with the mask 00001111, what is the result?
A
B
X

## Slide 6
Summary
The AND Gate
A Multisim circuit is shown. XWG1 is a word generator set in the count down mode. XLA1 is a logic analyzer with the output of the AND gate connected to first (upper) line of the analyzer. What signal do you expect to on this line?
Example
Solution
The output (line 1) will be HIGH only when all of the inputs are HIGH.

## Slide 7
The OR gate produces a HIGH output if any input is HIGH; if all inputs are LOW, the output is LOW. For a 2-input gate, the truth table is
Summary
The OR Gate
The OR operation is shown with a plus sign (+) between the variables. Thus, the OR operation is written as X = A + B.
0 0
0 1
1 0
1 1
0
1
1
1
A
B
X
A
B
X

## Slide 8
Summary
Example waveforms:
A
X
The OR operation can be used in computer programming to set certain bits of a binary number to 1.
The OR Gate
B
Example
A
B
X
A
B
X
ASCII letters have a 1 in the bit 5 position for lower case letters and a 0 in this position for capitals. (Bit positions are numbered from right to left starting with 0.) What will be the result if you OR an ASCII letter with the 8-bit mask 00100000?
Solution
The resulting letter will be lower case.

## Slide 9
Summary
The OR Gate
A Multisim circuit is shown. XWG1 is a word generator set to count down. XLA1 is a logic analyzer with the output
Example
Solution
The output (line 1) will be HIGH if any input is HIGH; otherwise it will be LOW.
connected to first (top) line of the analyzer. The three 2-input OR gates act as a single 4-input gate. What signal do you expect on the output line?

## Slide 10
The NAND gate produces a LOW output when all inputs are HIGH; otherwise, the output is HIGH. For a 2-input gate, the truth table is
Summary
The NAND Gate
0 0
0 1
1 0
1 1
1
1
1
0
A
B
X
A
B
X
The NAND operation is shown with a dot between the variables and an overbar covering them. Thus, the NAND operation is written as X = A .B (Alternatively, X = AB.)

## Slide 11
Summary
Example waveforms:
A
X
The NAND gate is particularly useful because it is a “universal” gate – all other basic gates can be constructed from NAND gates.
The NAND Gate
B
Question
How would you connect a 2-input NAND gate to form a basic inverter?
A
B
X
A
B
X

## Slide 12
Summary
The NAND Gate
A Multisim circuit is shown. XWG1 is a word generator set in the count up mode. A four-channel oscilloscope monitors the inputs and output. What output signal do you expect to see?
Example
Solution
The output (channel D) will be LOW only when all of the inputs are HIGH.
Inputs

## Slide 13
The NOR gate produces a LOW output if any input is HIGH; if all inputs are HIGH, the output is LOW. For a 2-input gate, the truth table is
Summary
The NOR Gate
0 0
0 1
1 0
1 1
1
0
0
0
A
B
X
A
B
X
The NOR operation is shown with a plus sign (+) between the variables and an overbar covering them. Thus, the NOR operation is written as X = A + B.

## Slide 14
Summary
Example waveforms:
A
X
The NOR operation will produce a LOW if any input is HIGH.
The NOR Gate
B
Example
When is the LED is ON for the circuit shown?
Solution
The LED will be on when all of the four inputs are HIGH.
A
B
X
A
B
X

## Slide 15
The XOR gate produces a HIGH output only when both inputs are at opposite logic levels. The truth table is
Summary
The XOR Gate
0 0
0 1
1 0
1 1
0
1
1
0
A
B
X
A
B
X
The XOR operation is written as X = AB + AB. Alternatively, it can be written with a circled plus sign between the variables as X = A + B.

## Slide 16
Summary
Example waveforms:
A
X
Notice that the XOR gate will produce a HIGH only when exactly one input is HIGH.
The XOR Gate
B
Question
If the A and B waveforms are both inverted for the above waveforms, how is the output affected?
There is no change in the output.
A
B
X
A
B
X

## Slide 17
The XNOR gate produces a HIGH output only when both inputs are at the same logic level. The truth table is
Summary
The XNOR Gate
0 0
0 1
1 0
1 1
1
0
0
1
A
B
X
A
B
X
The XNOR operation shown as X = AB + AB. Alternatively, the XNOR operation can be shown with a circled dot between the variables. Thus, it can be shown as X = A . B.

## Slide 18
Summary
Example waveforms:
A
X
Notice that the XNOR gate will produce a HIGH when both inputs are the same. This makes it useful for comparison functions.
The XNOR Gate
B
Question
If the A waveform is inverted but B remains the same, how is the output affected?
The output will be inverted.
A
B
X
A
B
X

## Slide 19
Two major fixed function logic families are TTL and CMOS. A third technology is BiCMOS, which combines the first two. Packaging for fixed function logic is shown.
Summary
Fixed Function Logic
DIP package SOIC package

## Slide 20
A dual in-line package (DIP) is an electronic device package with a rectangular housing and two parallel rows of electrical connecting pins. The package may be through-hole mounted to a printed circuit board or inserted in a socket.
Summary

## Slide 21
A small-outline integrated circuit (SOIC) is a surface-mounted integrated circuit (IC) package which occupies an area about 30–50% less than an equivalent DIP, with a typical thickness that is 70% less. They are generally available in the same pinouts as their counterpart DIP ICs.
Summary

## Slide 22
Some common gate configurations are shown.
Summary
Fixed Function Logic

## Slide 23
Logic symbols show the gates and associated pin numbers.
Summary
Fixed Function Logic

## Slide 24
Data sheets include limits and conditions set by the manufacturer as well as DC and AC characteristics. For example, some maximum ratings for a 74HC00A are:
Summary
Fixed Function Logic

## Slide 25
A Programmable Logic Device (PLD) can be programmed to implement logic. There are various technologies available for PLDs. Many use an internal array of AND gates to form logic terms. Many PLDs can be programmed multiple times.
Summary
Programmable Logic

## Slide 26
Summary
Programmable Logic
In general, the required logic for a PLD is developed with the aid of a computer. The logic can be entered using a Hardware Description Language (HDL) such as VHDL. Logic can be specified to the HDL as a text file, a schematic diagram, or a state diagram.
Example
A text entry for a programming a PLD in VHDL as a 2-input NAND gate is shown for reference in the following slide. In this case, the inputs and outputs are first specified. Then the signals are described. Although you are probably not familiar with VHDL, you can see that the program is simple to read.

## Slide 27
Summary
Programmable Logic
entity NandGate is
port(A, B: in bit;
LED: out bit);
end entity NandGate;
architecture GateBehavior of NandGate is
signal A, B: bit;
begin
X <= A nand B;
LED <= X;
end architecture GateBehavior;

## Slide 28
Selected Key Terms
Inverter
Truth table
Timing diagram
Boolean algebra
AND gate
A logic circuit that inverts or complements its inputs.
A table showing the inputs and corresponding output(s) of a logic circuit.
A diagram of waveforms showing the proper time relationship of all of the waveforms.
The mathematics of logic circuits.
A logic gate that produces a HIGH output only when all of its inputs are HIGH.

## Slide 29
Selected Key Terms
OR gate
NAND gate
NOR gate
Exclusive-OR gate
Exclusive-NOR gate
A logic gate that produces a HIGH output when one or more inputs are HIGH.
A logic gate that produces a LOW output only when all of its inputs are HIGH.
A logic gate that produces a LOW output when one or more inputs are HIGH.
A logic gate that produces a HIGH output only when its two inputs are at opposite levels.
A logic gate that produces a LOW output only when its two inputs are at opposite levels.

## Slide 30
The truth table for a 2-input AND gate is
© 2008 Pearson Education
Quiz
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
1
0
0
0
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
0
1
1
1
a.
b.
c.
d.
0
1
1
0
0
0
0
1

## Slide 31
The truth table for a 2-input NOR gate is
© 2008 Pearson Education
Quiz
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
a.
b.
c.
d.
0
1
1
0
0
0
0
1
1
0
0
0
0
1
1
1

## Slide 32
The truth table for a 2-input XOR gate is
© 2008 Pearson Education
Quiz
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
0 0
0 1
1 0
1 1
a.
b.
c.
d.
0
1
1
0
0
0
0
1
1
0
0
0
0
1
1
1

## Slide 33
© 2008 Pearson Education
Quiz
4. The symbol is for a(n)
a. OR gate
b. AND gate
c. NOR gate
d. XOR gate
A
B
X

## Slide 34
© 2008 Pearson Education
Quiz
5. The symbol is for a(n)
a. OR gate
b. AND gate
c. NOR gate
d. XOR gate
A
B
X

## Slide 35
© 2008 Pearson Education
Quiz
6. A logic gate that produces a HIGH output only when all of its inputs are HIGH is a(n)
a. OR gate
b. AND gate
c. NOR gate
d. NAND gate

## Slide 36
© 2008 Pearson Education
Quiz
7. The expression X = A + B means
a. A OR B
b. A AND B
c. A XOR B
d. A XNOR B

## Slide 37
© 2008 Pearson Education
Quiz
8. A 2-input gate produces the output shown. (X represents the output.) This is a(n)
a. OR gate
b. AND gate
c. NOR gate
d. NAND gate
A
X
B

## Slide 38
© 2008 Pearson Education
Quiz
9. A 2-input gate produces a HIGH output only when the inputs agree. This type of gate is a(n)
a. OR gate
b. AND gate
c. NOR gate
d. XNOR gate

## Slide 39
© 2008 Pearson Education
Quiz
10. The required logic for a PLD can be specified in an Hardware Description Language by
a. text entry
b. schematic entry
c. state diagrams
d. all of the above

## Slide 40
Answers:
1. c
2. b
3. a
4. a
5. d
6. b
7. c
8. d
9. d
10. d
Quiz