## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Chapter 5
© 2008 Pearson Education

## Slide 2
In Sum-of-Products (SOP) form, basic combinational circuits can be directly implemented with AND-OR combinations if the necessary complement terms are available.
Summary
Combinational Logic Circuits

## Slide 3
Summary
An example of an SOP implementation is shown. The SOP expression is an AND-OR combination of the input variables and the appropriate complements.
Combinational Logic Circuits
SOP
DE
ABC
A
B
C
E
D
X = ABC
+ DE

## Slide 4
When the output of a SOP form is inverted, the circuit is called an AND-OR-Invert circuit. The AOI configuration lends itself to product-of-sums (POS) implementation.
Summary
An example of an AOI implementation is shown. The output expression can be changed to a POS expression by applying DeMorgan’s theorem twice.
Combinational Logic Circuits
POS
DE
ABC
A
B
C
E
D
X = ABC
+ DE
X = ABC
+ DE
X = (A + B + C)(D + E)
X = (ABC)(DE)
AOI
DeMorgan

## Slide 5
The truth table for an exclusive-OR gate is
Summary
Exclusive-OR Logic
A
B
Notice that the output is HIGH whenever A and B disagree.
The Boolean expression is
The circuit can be drawn as
X
Symbols:
Distinctive shape Rectangular outline
X = AB + AB

## Slide 6
The truth table for an exclusive-NOR gate is
Summary
Exclusive-NOR Logic
A
B
Notice that the output is HIGH whenever A and B agree.
The Boolean expression is
The circuit can be drawn as
X
Symbols:
Distinctive shape Rectangular outline
X = AB + AB

## Slide 7
Summary
For each circuit, determine if the LED should be on or off.
(a) (b) (c)
Circuit (a): XOR, inputs agree, output is LOW, LED is ON.
Circuit (b): XNOR, inputs disagree, output is LOW, LED is ON.
Circuit (c): XOR, inputs disagree, output is HIGH, LED is OFF.
Example
Solution

## Slide 8
Implementing a SOP expression is done by first forming the AND terms; then the terms are ORed together.
Summary
Implementing Combinational Logic
Example
Solution
Show the circuit that will implement the Boolean expression X = ABC + ABD + BDE. (Assume that the variables and their complements are available.)
C
A
B
E
D
B
A
B
D
Start by forming the terms using three 3-input AND gates.
Then combine the three terms using a 3-input OR gate.
X = ABC + ABD + BDE

## Slide 9
For basic combinational logic circuits, the Karnaugh map can be read and the circuit drawn as a minimum SOP.
Summary
Karnaugh Map Implementation
Example
Solution
A Karnaugh map is drawn from a truth table. Read the minimum SOP expression and draw the circuit.
1. Group the 1’s into two overlapping groups as indicated.
Read each group by eliminating any variable that changes across a boundary.
B changes across this boundary
C changes across this boundary
The vertical group is read A C.
The horizontal group is read AB.
The circuit is on the next slide:

## Slide 10
Summary
Circuit:
C
A
A
C
A
+
A
B
Solution
continued…
X =
The result is shown as a sum of products.
It is a simple matter to implement this form using only NAND gates as shown in the text and following example.
B

## Slide 11
Summary
NAND Logic
Example
Convert the circuit in the previous example to one that uses only NAND gates.
Recall from Boolean algebra that double inversion cancels. By adding inverting bubbles to above circuit, it is easily converted to NAND gates:
C
A
B
A
C
A
+
A
B
X =
Solution

## Slide 12
Summary
NAND gates are sometimes called universal gates because they can be used to produce the other basic Boolean functions.
Universal Gates
Inverter
A
A
AND gate
A
B
AB
A
B
A + B
OR gate
A
B
A + B
NOR gate

## Slide 13
Summary
NOR gates are also universal gates and can form all of the basic gates.
Universal Gates
Inverter
A
A
OR gate
A
B
A + B
A
B
AB
AND gate
A
B
AB
NAND gate

## Slide 14
Summary
Recall from DeMorgan’s theorem that AB = A + B. By using equivalent symbols, it is simpler to read the logic of SOP forms. The earlier example shows the idea:
NAND Logic
C
A
B
A
C
A
+
A
B
X =
The logic is easy to read if you (mentally) cancel the two connected bubbles on a line.

## Slide 15
Summary
NOR Logic
B
A
C
A
X =
Again, the logic is easy to read if you (mentally) cancel the two connected bubbles on a line.
Alternatively, DeMorgan’s theorem can be written as A + B = A B. By using equivalent symbols, it is simpler to read the logic of POS forms. For example,
(A + B)(A + C)

## Slide 16
Summary
Pulsed Waveforms
For combinational circuits with pulsed inputs, the output can be predicted by developing intermediate outputs and combining the result. For example, the circuit shown can be analyzed at the outputs of the OR gates:
A
B
C
D
A
B
C
D
G1
G2
G3
G1
G2
G3

## Slide 17
Summary
Pulsed Waveforms
Alternatively, you can develop the truth table for the circuit and enter 0’s and 1’s on the waveforms. Then read the output from the table.
A
B
C
D
A
B
C
D
G1
G2
G3
G3
Inputs
A B C D
Output
0 0 0 0
0 0 0 1
0 0 1 0
0 0 1 1
0 1 0 0
0 1 0 1
0 1 1 0
0 1 1 1
1 0 0 0
1 0 0 1
1 0 1 0
1 0 1 1
1 1 0 0
1 1 0 1
1 1 1 0
1 1 1 1
0 1 0 1 0 1 0 1 0 1
0 1 1 0 0 1 1 0 0 0
0 0 0 1 1 1 1 0 0 0
0 0 0 0 0 0 0 1 1 0
0 0 0 0 1 1 1 0 1 0
X
0
1
1
1
0
1
1
1
0
0
0
0
0
1
1
1

## Slide 18
Selected Key Terms
Universal gate
Negative-OR
Negative-AND
Either a NAND or a NOR gate. The term universal refers to a property of a gate that permits any logic function to be implemented by that gate or by a combination of gates of that kind.
The dual operation of a NAND gate when the inputs are active-LOW.
The dual operation of a NOR gate when the inputs are active-LOW.

## Slide 19
© 2008 Pearson Education
Quiz
1. Assume an AOI expression is AB + CD. The equivalent POS expression is
a. (A + B)(C + D)
b. (A + B)(C + D)
c. (A + B)(C + D)
d. none of the above

## Slide 20
2. The truth table shown is for
a. a NAND gate
b. a NOR gate
c. an exclusive-OR gate
d. an exclusive-NOR gate
© 2008 Pearson Education
Quiz

## Slide 21
3. An LED that should be ON is
a. LED-1
b. LED-2
c. neither
d. both
© 2008 Pearson Education
Quiz

## Slide 22
© 2008 Pearson Education
Quiz
4. To implement the SOP expression , the type of gate that is needed is a
a. 3-input AND gate
b. 3-input NAND gate
c. 3-input OR gate
d. 3-input NOR gate
X = ABC + ABD + BDE
C
A
B
E
D
B
A
B
D

## Slide 23
© 2008 Pearson Education
Quiz
5. Reading the Karnaugh map, the logic expression is
a. A C + A B
b. A B + A C
c. A B + B C
d. A B + A C

## Slide 24
6. The circuit shown will have identical logic out if all gates are changed to
a. AND gates
b. OR gates
c. NAND gates
d. NOR gates
© 2008 Pearson Education
Quiz
A
B
C
D

## Slide 25
7. The two types of gates which are called universal gates are
a. AND/OR
b. NAND/NOR
c. AND/NAND
d. OR/NOR
© 2008 Pearson Education
Quiz

## Slide 26
8. The circuit shown is equivalent to an
a. AND gate
b. XOR gate
c. OR gate
d. none of the above
© 2008 Pearson Education
Quiz
A
B

## Slide 27
9. The circuit shown is equivalent to
a. an AND gate
b. an XOR gate
c. an OR gate
d. none of the above
© 2008 Pearson Education
Quiz
A
B

## Slide 28
10. During the first three intervals for the pulsed circuit shown, the output of
a. G1 is LOW and G2 is LOW
b. G1 is LOW and G2 is HIGH
c. G1 is HIGH and G2 is LOW
d. G1 is HIGH and G2 is HIGH
© 2008 Pearson Education
Quiz
A
B
C
D
A
B
C
D
G1
G2
G3

## Slide 29
Answers:
1. b
2. d
3. a
4. c
5. d
6. c
7. b
8. c
9. a
10. c
Quiz