## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Chapter 7
© 2008 Pearson Education
Notes: 1

## Slide 2
A latch is a temporary storage device that has two stable states (bistable). It is a basic form of memory.
Summary
Latches
The S-R (Set-Reset) latch is the most basic type. It can be constructed from NOR gates or NAND gates. With NOR gates, the latch responds to active-HIGH inputs; with NAND gates, it responds to active-LOW inputs.
NOR Active-HIGH Latch NAND Active-LOW Latch
R
S
Q
Q
Q
S
R
Q
Notes: 2

## Slide 3
The active-HIGH S-R latch is in a stable (latched) condition when both inputs are LOW.
Summary
Latches
R
S
Q
Q
Assume the latch is initially RESET (Q = 0) and the inputs are at their inactive level (0). To SET the latch (Q = 1), a momentary HIGH signal is applied to the S input while the R remains LOW.
0
1
0
R
S
Q
Q
1
0
0
To RESET the latch (Q = 0), a momentary HIGH signal is applied to the R input while the S remains LOW.
0
0
1
0
1
0
Latch initially RESET
Latch initially SET
Notes: 3

## Slide 4
S
R
The active-LOW S-R latch is in a stable (latched) condition when both inputs are HIGH.
Summary
Latches
Q
Q
1
1
0
1
0
1
Latch initially RESET
Q
Q
1
1
0
1
0
1
Latch initially SET
S
R
Assume the latch is initially RESET (Q = 0) and the inputs are at their inactive level (1). To SET the latch (Q = 1), a momentary LOW signal is applied to the S input while the R remains HIGH.
To RESET the latch a momentary LOW is applied to the R input while S is HIGH.
Never apply an active set and reset at the same time (invalid).
Notes: 4

## Slide 5
Truth table & Logic symbol
Summary
Latches
Notes: 5

## Slide 6
The active-LOW S-R latch is available as the 74LS279A IC.
Summary
Latches
1Q
2Q
3Q
4Q
74LS279A
It features four internal latches with two having two S inputs. To SET any of the latches, the S line is pulsed low. It is available in several packages.
Position 1 to 2
Position 2 to 1
S
R
Q
VCC
S-R latches are frequently used for switch debounce circuits as shown:
S
R
Notes: 6

## Slide 7
A gated latch is a variation on the basic latch.
Summary
Latches
The gated latch has an additional input, called enable (EN) that must be HIGH in order for the latch to respond to the S and R inputs.
R
S
Q
Q
EN
Show the Q output with relation to the input signals. Assume Q starts LOW.
Example
Solution
Keep in mind that S and R are only active when EN is HIGH.
S
R
EN
Q
S
R
Notes: 7

## Slide 8
Summary
Latches
The D latch is an variation of the S-R latch but combines the S and R inputs into a single D input as shown:
A simple rule for the D latch is:
Q follows D when the Enable is active.
D
EN
Q
Q
Q
Q
D
EN
Notes: 8

## Slide 9
Summary
Latches
The truth table for the D latch summarizes its operation. If EN is LOW, then there is no change in the output and it is latched.
Notes: 9

## Slide 10
Summary
Latches
Determine the Q output for the D latch, given the inputs shown.
Notice that the Enable is not active during these times, so the output is latched.
Q
Q
D
EN
Example
Notes: 10

## Slide 11
Summary
Synchronous & Asynchronous Circuits
Digital circuits can operate synchronously or asynchronously.
Asynchronous circuits are more difficult to design & manage.
In synchronous circuits, the Clock is the synchronizing signal.
Clock is a rectangular or square pulse train.
Notes: 11

## Slide 12
Summary
Flip-flops
A flip-flop differs from a latch in the manner it changes states. A flip-flop is a clocked device, in which only the clock edge determines when a new bit is entered.
The active edge can be positive or negative.
Dynamic input indicator
Notes: 12

## Slide 13
Summary
S-R Flip-flop
S-R FFs are not available as ICs but are building blocks of other flip-flops.
S and R inputs of the S-R FF are called synchronous inputs because they are synchronized with the clock.
S-R FF can be positive or negative edge triggered.
1
1
0
0
0
0
1
0
= Q0
Notes: 13

## Slide 14
Summary
S-R Flip-flop
A simplified diagram of a positive edge-triggered S-R flip-flop
Gated latch, encountered few slides earlier.
Notes: 14

## Slide 15
Summary
S-R Flip-flop
1
1
0
0
0
0
1
0
= Q0
Inputs |  |  | Outputs |  | 
S | R | CLK | Q | Q’ | Comments
0 | 0 |  | Q0 | Q’0 | No Change
0 | 1 |  | 0 | 1 | RESET
1 | 0 |  | 1 | 0 | SET
1 | 1 |  | ? | ? | Invalid
Notes: 15

## Slide 16
Summary
S-R Flip-flop
Inputs |  |  | Outputs |  | 
S | R | CLK | Q | Q’ | Comments
0 | 0 |  | Q0 | Q0’ | No Change
0 | 1 |  | 0 | 1 | RESET
1 | 0 |  | 1 | 0 | SET
1 | 1 |  | ? | ? | Invalid
Notes: 16

## Slide 17
Summary
D Flip-flop
D
The D-flip flop has only one input.
D flip-flop is useful when a single bit is to be stored.
Basic principle - Q follows D at the active or triggering clock edge.
Positive edge-triggered ff formed with a S-R ff and an inverter
Notes: 17

## Slide 18
Summary
D Flip-flop
The truth table for a positive-edge triggered D flip-flop shows an up arrow to show that it is sensitive to its D input only on the rising edge of the clock; otherwise it is latched. The truth table for a negative-edge triggered D flip-flop is identical except for the direction of the arrow.
(a) Positive-edge triggered (b) Negative-edge triggered
Notes: 18

## Slide 19
Summary
D Flip-flop
Positive-edge triggered
Notes: 19

## Slide 20
Summary
J-K Flip-flop
The J-K flip-flop is more versatile than the D flip flop. In addition to the clock input, it has two inputs, labeled J and K. When both J and K = 1, the output changes states (toggles) on the active clock edge (in this case, the rising edge).
Notes: 20

## Slide 21
Summary
J-K Flip-flop
Notes: 21

## Slide 22
Summary
JK Flip-flop
Determine the Q output for the J-K flip-flop, given the inputs shown.
Example
CLK
Q
K
J
Solution
Set
Toggle
Set
Latch
Notes: 22

## Slide 23
Summary
Flip-flops
CLK
D
CLK
Q
Q
A D-flip-flop does not have a toggle mode like the J-K flip-flop, but you can hardwire a toggle mode by connecting Q back to D as shown. This is useful in some counters as you will see in Chapter 8.
For example, if Q is LOW, Q is HIGH and the flip-flop will toggle on the next clock edge. Because the flip-flop only changes on the active edge, the output will only change once for each clock pulse.
D flip-flop hardwired for a toggle mode
Notes: 23

## Slide 24
Summary
Asynchronous Inputs
Synchronous inputs are transferred in the triggering edge of the clock (for example the D or J-K inputs). Most flip-flops have other inputs that are asynchronous, meaning they affect the output independent of the clock.
Two such inputs are normally labeled preset (PRE) and clear (CLR). These inputs are usually active LOW. A J-K flip flop with active LOW preset and CLR is shown.
CLK
K
J
Q
Q
PRE
CLR
Notes: 24

## Slide 25
Summary
Flip-flops
Asynchronous Inputs
Determine the Q output for the J-K flip-flop, given the inputs shown.
Example
CLK
K
J
Q
Q
PRE
CLR
Solution
Set
Toggle
Reset
Toggle
Set
Set
Reset
Latch
CLK
K
J
Q
PRE
CLR
Notes: 25

## Slide 26
Propagation delay time is specified for the rising and falling outputs. It is measured between the 50% level of the clock to the 50% level of the output transition.
Summary
Flip-flop Characteristics
50% point on triggering edge
50% point
50% point on LOW-to-HIGH transition of Q
tPLH
tPHL
CLK
CLK
Q
Q
50% point on HIGH-to- LOW transition of Q
The typical propagation delay time for the 74AHC family (CMOS) is 4 ns. Even faster logic is available for specialized applications.
Notes: 26

## Slide 27
Another propagation delay time specification is the time required for an asynchronous input to cause a change in the output. Again it is measured from the 50% levels. The 74AHC family has specified delay times under 5 ns.
Summary
Flip-flop Characteristics
50% point
tPLH
tPHL
Q
50% point
50% point
50% point
Q
PRE
CLR
Notes: 27

## Slide 28
Set-up time and hold time are times required before and after the clock transition that data must be present to be reliably clocked into the flip-flop.
Summary
Flip-flop Characteristics
Setup time is the minimum time for the data to be present before the clock.
Hold time is the minimum time for the data to remain after the clock.
CLK
D
CLK
D
Set-up time, ts
Hold time, tH
Notes: 28

## Slide 29
Other specifications include maximum clock frequency, minimum pulse widths for various inputs, and power dissipation. The power dissipation is the product of the supply voltage and the average current required.
Summary
Flip-flop Characteristics
A useful comparison between logic families is the speed-power product which uses two of the specifications discussed: the average propagation delay and the average power dissipation. The unit is energy.
Example
Solution
What is the speed-power product for 74AHC74A? Use the data from Table 7-5 to determine the answer.
From Table 7-5, the average propagation delay is 4.6 ns. The quiescent power dissipated is 1.1 mW. Therefore, the speed-power product is
5 pJ
Notes: 29

## Slide 30
Summary
Flip-flop Applications
Principal flip-flop applications are for temporary data storage, as frequency dividers, and in counters (which are covered in detail in Chapter 8).
Typically, for data storage applications, a group of flip-flops are connected to parallel data lines and clocked together. Data is stored until the next clock pulse.
Parallel data input lines
Clock
Clear
Output lines
Q0
Q1
Q2
Q3
Notes: 30

## Slide 31
Summary
Flip-flop Applications
For frequency division, it is simple to use a flip-flop in the toggle mode or to chain a series of toggle flip flops to continue to divide by two.
One flip-flop will divide fin by 2, two flip-flops will divide fin by 4 (and so on). A side benefit of frequency division is that the output has an exact 50% duty cycle.
HIGH
HIGH
CLK
K
J
QA
CLK
K
J
fin
QB
fout
Waveforms:
fin
fout
Notes: 31

## Slide 32
Summary
One-Shots
The one-shot or monostable multivibrator is a device with only one stable state. When triggered, it goes to its unstable state for a predetermined length of time, then returns to its stable state.
For most one-shots, the length of time in the unstable state (tW) is determined by an external RC circuit.
Trigger
CEXT
REXT
+V
CX
RX/CX
Q
Q
tW
Trigger
Q
Notes: 32

## Slide 33
Summary
One-Shots
Retriggerable one-shots respond to any trigger, even if it occurs in the unstable state. If it occurs during the unstable state, the state is extended by an amount equal to the pulse width.
Retriggers
tW
Trigger
Q
Retriggerable one-shot:
Nonretriggerable one-shots do not respond to any triggers that occur during the unstable state.
Notes: 33

## Slide 34
Summary
One-Shots
An application for a retriggerable one-shot is a power failure detection circuit. Triggers are derived from the ac power source, and continue to retrigger the one shot. In the event of a power failure, the one-shot is not triggered and an alarm can be initiated.
tW
tW
tW
Retriggers
Retriggers
Triggers derived from ac
Q
Missing trigger due to power failure
Power failure indication
Notes: 34

## Slide 35
Summary
The 555 timer
The 555 timer can be configured in various ways, including as a one-shot. A basic one shot is shown. The pulse width is determined by R1C1 and is approximately tW = 1.1R1C1.
The trigger is a negative-going pulse.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
tW = 1.1R1C1
C1
R1
Notes: 35

## Slide 36
Summary
The 555 timer
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
tW = 1.1R1C1
C1
R1
Determine the pulse width for the circuit shown.
Example
Solution
tW = 1.1R1C1 = 1.1(10 kW)(2.2 mF) =
10 kW
2.2 mF
24.2 ms
+15 V
Notes: 36

## Slide 37
Summary
The 555 timer
The 555 can be configured as a basic astable multivibrator with the circuit shown. In this circuit C1 charges through R1 and R2 and discharges through only R2. The output frequency is given by:
The frequency and duty cycle are set by these components.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
C1
R1
R2
+VCC
Notes: 37

## Slide 38
Summary
The 555 timer
Given the components, you can read the frequency from the chart. Alternatively, you can use the chart to pick components for a desired frequency.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
C1
R1
R2
+VCC
C1 (mF)
f (Hz)
Notes: 38

## Slide 39
Selected Key Terms
Latch
Bistable
Clock
D flip-flop
J-K flip-flop
A bistable digital circuit used for storing a bit.
Having two stable states. Latches and flip-flops are bistable multivibrators.
A triggering input of a flip-flop.
A type of bistable multivibrator in which the output assumes the state of the D input on the triggering edge of a clock pulse.
A type of flip-flop that can operate in the SET, RESET, no-change, and toggle modes.
Notes: 39

## Slide 40
Selected Key Terms
Propagation delay time
Set-up time
Hold time
Timer
The interval of time required after an input signal has been applied for the resulting output signal to change.
The time interval required for the input levels to be on a digital circuit.
The time interval required for the input levels to remain steady to a flip-flop after the triggering edge in order to reliably activate the device.
A circuit that can be used as a one-shot or as an oscillator.
Notes: 40

## Slide 41
1. The output of a D latch will not change if
a. the output is LOW
b. Enable is not active
c. D is LOW
d. all of the above
© 2008 Pearson Education
Quiz
Notes: 41

## Slide 42
2. The D flip-flop shown will
a. set on the next clock pulse
b. reset on the next clock pulse
c. latch on the next clock pulse
d. toggle on the next clock pulse
© 2008 Pearson Education
Quiz
CLK
D
CLK
Q
Q
Notes: 42

## Slide 43
3. For the J-K flip-flop shown, the number of inputs that are asynchronous is
a. 1
b. 2
c. 3
d. 4
© 2008 Pearson Education
Quiz
CLK
K
J
Q
Q
PRE
CLR
Notes: 43

## Slide 44
4. Assume the output is initially HIGH on a leading edge triggered J-K flip flop. For the inputs shown, the output will go from HIGH to LOW on which clock pulse?
a. 1
b. 2
c. 3
d. 4
© 2008 Pearson Education
Quiz
CLK
K
J
1 2 3 4
Notes: 44

## Slide 45
5. The time interval illustrated is called
a. tPHL
b. tPLH
c. set-up time
d. hold time
© 2008 Pearson Education
Quiz
50% point on triggering edge
50% point on LOW-to-HIGH transition of Q
CLK
Q
?
Notes: 45

## Slide 46
© 2008 Pearson Education
Quiz
CLK
D
?
6. The time interval illustrated is called
a. tPHL
b. tPLH
c. set-up time
d. hold time
Notes: 46

## Slide 47
7. The application illustrated is a
a. astable multivibrator
b. data storage device
c. frequency multiplier
d. frequency divider
© 2008 Pearson Education
Quiz
HIGH
HIGH
CLK
K
J
QA
CLK
K
J
fin
QB
fout
Notes: 47

## Slide 48
© 2008 Pearson Education
Quiz
8. The application illustrated is a
a. astable multivibrator
b. data storage device
c. frequency multiplier
d. frequency divider
Parallel data input lines
Clock
Clear
Output lines
Q0
Q1
Q2
Q3
Notes: 48

## Slide 49
9. A retriggerable one-shot with an active HIGH output has a pulse width of 20 ms and is triggered from a 60 Hz line. The output will be a
a. series of 16.7 ms pulses
b. series of 20 ms pulses
c. constant LOW
d. constant HIGH
© 2008 Pearson Education
Quiz
Notes: 49

## Slide 50
© 2008 Pearson Education
Quiz
10. The circuit illustrated is a
a. astable multivibrator
b. monostable multivibrator
c. frequency multiplier
d. frequency divider
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
C1
R1
R2
Notes: 50

## Slide 51
Answers:
1. b
2. d
3. b
4. c
5. b
6. d
7. d
8. b
9. d
10. a
Quiz
Notes: 51