## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Chapter 8
© 2008 Pearson Education

## Slide 2
As you know, the binary count sequence follows a familiar pattern of 0’s and 1’s as described in Section 2-2 of the text.
LSB changes on every number.
The next bit changes on every other number.
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The next bit changes on every fourth number.
Summary
Counting in Binary

## Slide 3
A counter can form the same pattern of 0’s and 1’s with logic levels. The first stage in the counter represents the least significant bit – notice that these waveforms follow the same pattern as counting in binary.
LSB
MSB
Summary
Counting in Binary

## Slide 4
In a 2-bit asynchronous counter, the clock is applied only to the first stage. Second stage derive the clock from the previous stage.
Summary
Two bit Asynchronous Counter

## Slide 5
In an asynchronous counter, the clock is applied only to the first stage. Subsequent stages derive the clock from the previous stage.
Summary
Three bit Asynchronous Counter
The three-bit asynchronous counter shown is typical. It uses J-K flip-flops in the toggle mode.
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH
Waveforms are on the following slide…

## Slide 6
Summary
Three bit Asynchronous Counter
CLK
Q0
Q1
Q2
Notice that the Q0 output is triggered on the leading edge of the clock signal. The following stage is triggered from Q0. The leading edge of Q0 is equivalent to the trailing edge of Q0. The resulting sequence is that of an 3-bit binary up counter.

## Slide 7
Summary
Propagation Delay
Asynchronous counters are sometimes called ripple counters, because the stages do not all change together. For certain applications requiring high clock rates, this is a major disadvantage.
Notice how delays are cumulative as each stage in a counter is clocked later than the previous stage.
CLK
Q0
Q1
Q2
Q0 is delayed by 1 propagation delay, Q2 by 2 delays and Q3 by 3 delays.

## Slide 8
Summary
Truncated Counters
Counter Modulus: The number of unique states through which the counter will sequence.
Max possible states (Max Mod) = 2n (where n is total FFs)
Truncated counters: Counters that count less than the maximum modulus (max states). Less than max states sequence is called truncated sequence.
MOD10 or Decade counters: Counters that count 10 distinct states.
Decade counter with sequence from 0000 to 1001 is a BCD decade counter.

## Slide 9
Summary
Asynchronous Decade Counter
This counter uses partial decoding to recycle the count sequence to zero after the 1001 state. The flip-flops are trailing-edge triggered, so clocks are derived from the Q outputs. Other truncated sequences can be obtained using a similar technique.
Waveforms are on the following slide…
CLK
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
HIGH
C
J3
K3
Q3
CLR

## Slide 10
Summary
Asynchronous Decade Counter
When Q1 and Q3 are HIGH together, the counter is cleared by a “glitch” on the CLR line.
CLK
Q0
Q1
Q2
Q3
CLR
Glitch
Glitch

## Slide 11
Summary
Class Exercise - Asynchronous Truncated Counters
This counter uses partial decoding to recycle the count sequence to zero after the 1001 state. The flip-flops are trailing-edge triggered, so clocks are derived from the Q outputs. Other truncated sequences can be obtained using a similar technique.
CLK
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
HIGH
C
J3
K3
Q3
CLR

## Slide 12
Summary
Asynchronous Counter Using D Flip-flops
D flip-flops can be set to toggle and used as asynchronous counters by connecting Q back to D. The counter in this slide is a Multisim simulation of one described in the lab manual. Can you figure out the sequence?
The next slide shows the scope…
MSB
LSB
Q to D puts D flip-flop in toggle mode

## Slide 13
Summary
CLR
CLK
LSB
MSB
The sequence is 0 – 2 – 1 – (CLR) (repeat)…
Note that it is momentarily in state 3 which causes it to clear.

## Slide 14
Summary
The 74LS93A Asynchronous Counter
The 74LS93A has one independent toggle J-K flip-flop driven by CLK A and three toggle J-K flip-flops that form an asynchronous counter driven by CLK B.
CLK A
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
C
J3
K3
Q3
CLK B
The counter can be extended to form a 4-bit counter by connecting Q0 to the CLK B input. Two inputs are provided that clear the count.
RO (1)
RO (2)
All J and K inputs are connected internally HIGH

## Slide 15
Summary
Synchronous Counters
In a synchronous counter all flip-flops are clocked together with a common clock pulse.
The most important advantage of synchronous counters is that there is no cumulative time delay because all flip-flops are triggered in parallel. Thus, the maximum operating frequency for this counter will be significantly higher than for the corresponding ripple counter.
Synchronous counters generally require more circuitry to control states changes.

## Slide 16
Summary
2-bit Synchronous Counter
Q1
Q1

## Slide 17
Summary
3-bit Synchronous Counter
1 2 3 4 5 6 7 8
0
0
0
1
0
0
0
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
1
0
0
0
0
FF0
FF1
FF2

## Slide 18
Summary
3-bit Synchronous Counter
This 3-bit binary synchronous counter has the same count sequence as the 3-bit asynchronous counter shown previously
K0
J0
Q0
C
C
C
J1
J2
K1
K2
Q0Q1
Q0
Q1
Q2
CLK
HIGH

## Slide 19
Summary
Analysis of Synchronous Counters
A tabular technique for analysis is illustrated for the counter on the previous slide. Start by setting up the outputs as shown, then write the logic equation for each input. This has been done for the counter.
Q2 Q1 Q0 | J2 = Q0Q1 | K2 = Q0Q1 | J1 = Q0 | K1 = Q0 | J0 = 1 | K0 = 1
Outputs
Logic for inputs
1. Put the counter in an arbitrary state; then determine the inputs for this state.
0 0 0
0
0
0
0
1
1
2. Use the new inputs to determine the next state: Q2 and Q1 will latch and Q0 will toggle.
0 0 1
0
0
1
1
1
1
3. Set up the next group of inputs from the current output.
Continue like this, to complete the table. The next slide shows the completed table…
0 1 0
4. Q2 will latch again but both Q1 and Q0 will toggle.

## Slide 20
Summary
Analysis of Synchronous Counters
Outputs
Logic for inputs
0 0 0
0
0
0
0
1
1
0 0 1
0
0
1
1
1
1
0 1 0
Q2 Q1 Q0 | J2 = Q0Q1 | K2 = Q0Q1 | J1 = Q0 | K1 = Q0 | J0 = 1 | K0 = 1
1
1
1
1
1
1
1
1
1
1
1
1
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
0
0
0
0
1
1
1
1
0
0
0
0
0
0
1
1
0
0
0
0
1
1
1
1
At this points all states have been accounted for and the counter is ready to recycle…

## Slide 21
Summary
A 4-bit Synchronous Binary Counter
Q1Q0 = 11
Q2Q1Q0 = 111

## Slide 22
Summary
A 4-bit Synchronous Binary Counter
Q0
Q1
Q2
Q3
The 4-bit binary counter has one more AND gate than the 3-bit counter just described. The shaded areas show where the AND gate outputs are HIGH causing the next FF to toggle.

## Slide 23
BCD synchronous decade counter counts from 0000 to 1001, then recycles to 0000.
Summary
BCD Decade Counter
J0 = K0 = 1
J1 = K1 = Q0Q3
J2 = K2 = Q0Q1
J3 = K3 = Q0Q1Q2 + Q0Q3
?
?
?
?
Input conditions / logic equations at different counter stages:

## Slide 24
With some additional logic, a binary counter can be converted to a BCD synchronous decade counter. After reaching the count 1001, the counter recycles to 0000.
This gate detects 1001, and causes FF3 to toggle on the next clock pulse. FF0 toggles on every clock pulse. Thus, the count starts over at 0000.
Summary
BCD Decade Counter
Q0
Q3

## Slide 25
Waveforms for the decade counter:
Summary
BCD Decade Counter
These same waveforms can be obtained with an asynchronous counter in IC form – the 74LS90. It is available in a dual version – the 74LS390, which can be cascaded. It is slower than synchronous counters (max count frequency is 35 MHz), but is simpler.
CLK
Q0
Q1
Q2
Q3

## Slide 26
Summary
A 4-bit Synchronous Binary Counter
The 74LS163 is a 4-bit IC synchronous counter with additional features over a basic counter. It has parallel load, a CLR input, two chip enables, and a ripple count output that signals when the count has reached the terminal count.
Example waveforms are on the next slide…
Data inputs
Data outputs
CLR
LOAD
ENT
ENP
CLK
RCO
Q0
Q1
Q2
Q3
D0
D1
D2
D3

## Slide 27
Summary
Data inputs
Data outputs
CLR
LOAD
ENT
ENP
CLK
RCO
Q0
Q1
Q2
Q3
D0
D1
D2
D3
Clear Preset
Count Inhibit
12 13 14 15 0 1 2

## Slide 28
Summary
Up/Down Synchronous Counters
An up/down counter is capable of progressing in either direction depending on a control input.
CLK
Q0
Q1
Q2
K0
J0
C
C
C
J1
J2
K1
K2
HIGH
UP/DOWN
UP
DOWN
FF0
FF1
FF2
Q0.UP
Q0.DOWN
Q0
Q1
Q2

## Slide 29
Summary
Compare Up/Down Counters with Simple Up counter
Implement Up logic as shown
Duplicate the Down Logic on
same grounds

## Slide 30
Summary
Up/Down Synchronous Counter Analysis
Clock Pulse | UP | Q2 | Q1 | Q0 | DOWN
0 | ↘ | 0 | 0 | 0 | ↖
1 | ↘ | 0 | 0 | 1 | ↖
2 | ↘ | 0 | 1 | 0 | ↖
3 | ↘ | 0 | 1 | 1 | ↖
4 | ↘ | 1 | 0 | 0 | ↖
5 | ↘ | 1 | 0 | 1 | ↖
6 | ↘ | 1 | 1 | 0 | ↖
7 | ↘ | 1 | 1 | 1 | ↖
The J and K inputs of different FFs must equal 1 (HIGH) under the conditions expressed by the following equations to make them toggle:
J0 = K0 = 1
J1 = K1 = (Q0 • UP) + (Q0 • DOWN)
J2 = K2 = (Q0 • Q1 • UP) + (Q0 • Q1 • DOWN)

## Slide 31
Summary
Up/Down Synchronous Counters
CLK
Q0
Q1
Q2
K0
J0
C
C
C
J1
J2
K1
K2
HIGH
UP/DOWN
UP
DOWN
FF0
FF1
FF2
Q0.UP
Q0.DOWN
Q0
Q1
Q2
J0 = K0 = 1
J1 = K1 = (Q0 • UP) + (Q0 • DOWN)
J2 = K2 = (Q0 • Q1 • UP) + (Q0 • Q1 • DOWN)

## Slide 32
Summary
Up/Down Synchronous Counters
UP/DOWN
Q0
Q1
Q2
Count up
Count down

## Slide 33
Summary
Up/Down Synchronous Counters
˄
˄
˄
˄
˄
˄
˄
˄
˄
˄
˄
˄
1
0
1
0
1
0
1
0
Plot counter output

## Slide 34
Summary
Up/Down Synchronous Counters
The 74HC191 has the same inputs and outputs but is a synchronous up/down binary counter.
Data inputs
Data outputs
MAX/MIN
CLK
Q0
Q1
Q2
Q3
LOAD
CTEN
RCO
D/U
D0
D1
D2
D3
C
CTR DIV 10
74HC190
Data inputs
Data outputs
MAX/MIN
CLK
Q0
Q1
Q2
Q3
LOAD
CTEN
RCO
D/U
D0
D1
D2
D3
C
CTR DIV 16
74HC191
The 74HC190 is a high speed CMOS synchronous up/down decade counter with parallel load capability. It also has a active LOW ripple clock output (RCO) and a MAX/MIN output when the terminal count is reached.

## Slide 35
Summary
Gray Code Counter Design
Required Flip-flops  3. No undesired states.
State diagram:
Next state table:

## Slide 36
Summary
Towards Gray Code Excitation Table
Transition Table

## Slide 37
Summary
Gray Code Excitation Table
Q2 | Q1 | Q0 | J0 | K0 | J1 | K1 | J2 | K2
0 | 0 | 0 | 1 | X | 0 | X | 0 | X
0 | 0 | 1 | X | 0 | 1 | X | 0 | X
0 | 1 | 1 | X | 1 | X | 0 | 0 | X
0 | 1 | 0 | 0 | X | X | 0 | 1 | X
1 | 1 | 0 | 1 | X | X | 0 | X | 0
1 | 1 | 1 | X | 0 | X | 1 | X | 0
1 | 0 | 1 | X | 1 | 0 | X | X | 0
1 | 0 | 0 | 0 | X | 0 | X | X | 1

## Slide 38
Summary
Gray Code Counter Design
Use K-Map to determine equations for J0, K0, J1, K1, J2 and K2
Q1Q2 + Q1Q2
Q1Q2 + Q1Q2

## Slide 39
Summary
Gray Code Counter Design
Use K-Map to determine equations for J0, K0, J1, K1, J2 and K2
Q0Q2
Q0Q2

## Slide 40
Summary
Gray Code Counter Design
Use K-Map to determine equations for J0, K0, J1, K1, J2 and K2
Q0Q1
Q0Q1

## Slide 41
Summary
Gray Code Counter Design
Equations for J0, K0, J1, K1, J2 and K2
J0 = Q1Q2 + Q1Q2
K0 = Q1Q2 + Q1Q2
J1 = Q0Q2
K1 = Q0Q2
J2 = Q0Q1
K2 = Q0Q1

## Slide 42
Summary
Gray Code Counter
CLK
Q0
Q1
Q2
K0
J0
C
C
C
J1
J2
K1
K2
FF0
FF1
FF2
Q0
Q1
Q2
The circuit can be checked with Cedarlogic before constructing it.

## Slide 43
Summary
Q0
Q1
Q2
Gray Code Counter

## Slide 44
Design a MOD-6 synchronous counter which follow the count sequence 000 , 010 , 011 , 001 , 100 , 110 , 000 , 010 …….
Summary
Counters with Arbitrary Sequences
Step -1
Determine the number of flip-flops required for the purpose. Identify the undesired states. In the present case, the number of flip-flops required is 3 and the undesired states are 101 and 111

## Slide 45
Summary
Counters with Arbitrary Sequences
Step - 2
Draw the state transition diagram showing all possible states including the ones that are not desired. The undesired states should be depicted to be transiting to any of the desired states. We have chosen the 000 state for this purpose. It is important to include the undesired states to ensure that, if the counter accidentally gets into any of these undesired states, it will go to a desired state to resume the correct sequence on application of the next clock pulse.

## Slide 46
Summary
Counters with Arbitrary Sequences
Step – 2 State Transition Diagram

## Slide 47
Summary
Counters with Arbitrary Sequences
Step – 3
Draw the excitation table for the counter, listing the present states, the next states corresponding to the present states and the required logic status of the flip-flop inputs (the J and K inputs).

## Slide 48
Summary
Counters with Arbitrary Sequences
JK Truth Table
J-K transition table

## Slide 49
Summary
Counters with Arbitrary Sequences
Step – 3 Excitation Table

## Slide 50
Summary
Counters with Arbitrary Sequences
Step – 4
Generate JA, KA, JB, KB, JC and KC inputs from available A, A’, B, B’, C and C’ outputs of FFs.
This is done by drawing Karnaugh maps for each one of the inputs, minimizing them and writing Boolean equations.

## Slide 51
Summary
Counters with Arbitrary Sequences
Step – 4 Karnaugh Mapping - JA

## Slide 52
Summary
Counters with Arbitrary Sequences
Step – 4 Karnaugh Mapping - KA

## Slide 53
Summary
Counters with Arbitrary Sequences
Step – 4 Karnaugh Mapping - JB

## Slide 54
Summary
Counters with Arbitrary Sequences
Step – 4 Karnaugh Mapping - KB

## Slide 55
Summary
Counters with Arbitrary Sequences
Step – 4 Karnaugh Mapping - JC

## Slide 56
Summary
Counters with Arbitrary Sequences
Step – 4 Karnaugh Mapping - KC

## Slide 57
Summary
Counters with Arbitrary Sequences
Step – 5
When all input conditions are obtained, a circuit can be drawn that will produce the desired output. The circuit can be tested in software before implementation.

## Slide 58
Summary
Counters with Arbitrary Sequences
Step – 5

## Slide 59
HIGH
CLK
Q0
Q1
Q2
C
Counter 1
Counter 2
C
CTEN
CTEN
CTR DIV 16
CTR DIV 16
Q3
Q0
Q1
Q2
Q3
TC
TC
fin
Example
Solution
a) Each counter divides the frequency by 16. Thus the modulus is 162 = 256.
Cascading is a method of achieving higher-modulus counters. For synchronous IC counters, the next counter is enabled only when the terminal count of the previous stage is reached.
Summary
Cascaded counters
What is the modulus of the cascaded DIV 16 counters?
If fin =100 kHz, what is fout?
fout
b) The output frequency is 100 kHz/256 = 391 Hz

## Slide 60
Decoding is the detection of a binary number and can be done with an AND gate.
Summary
Counter Decoding
Question
What number is decoded by this gate?

## Slide 61
The decade counter shown previously incorporates partial decoding (looking at only the MSB and the LSB) to detect 1001. This was possible because this is the first occurrence of this combination in the sequence.
Summary
Partial Decoding
Detects 1001 by looking only at two bits

## Slide 62
The divide-by-60 counter in the text also uses partial decoding to clear the tens count when a 6 was detected.
The divide characteristic illustrated here is a good way to obtain a lower frequency using a counter. For example, the 60 Hz power line can be converted to 1 Hz.
Summary
Resetting the Count with a Decoder

## Slide 63
Show how to decode state 5 with an active LOW output.
Notice that a NAND gate was used to give the active LOW output.
Summary
Counter Decoding
Example
Solution

## Slide 64
Summary
Logic Symbols
Dependency notation allows the logical operation of a device to be determined from its logic symbol.
CLK
Q0
LOAD
RCO
D0
D1
D2
D3
ENT
D0
D1
D2
D3
Q0
Q1
Q2
Q3
RCO
CLR
ENP
CLK
ENT
ENP
LOAD
CLR
C
C5/2,3,4
5CT = 0
M1
M2
G3
G4
CTR DIV 16
CTR DIV 16
Common control block
Q1
Q2
Q3

## Slide 65
Selected Key Terms
Asynchronous
Modulus
Synchronous
Terminal count
State machine
Cascade
Not occurring at the same time.
The number of unique states through which a counter will sequence.
Occurring at the same time.
The final state in a counter’s sequence.
A logic system exhibiting a sequence of states or values.
To connect “end-to-end” as when several counters are connected from the terminal count output of one to the enable input of the next counter.

## Slide 66
1. The counter shown below is an example of
a. an asynchronous counter
b. a BCD counter
c. a synchronous counter
d. none of the above
© 2008 Pearson Education
Quiz
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH

## Slide 67
The Q0 output of the counter shown
a. is present before Q1 or Q2
b. changes on every clock pulse
c. has a higher frequency than Q1 or Q2
d. all of the above
© 2008 Pearson Education
Quiz
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH

## Slide 68
3. To cause a D flip-flop to toggle, connect the
a. clock to the D input
b. Q output to the D input
c. Q output to the D input
d. clock to the preset input
© 2008 Pearson Education
Quiz

## Slide 69
4. The 7493A asynchronous counter diagram is shown (J’s and K’s are HIGH.) To make the count have a modulus of 16, connect
a. Q0 to RO(1) and RO(2) to
b. Q3 to RO(1) and RO(2)
c. CLK A and CLK B together
d. Q0 to CLK B
Quiz
© 2008 Pearson Education

## Slide 70
© 2008 Pearson Education
Quiz
FF0
FF1
FF2
5. Assume Q0 is LOW. The next clock pulse will cause
a. FF1 and FF2 to both toggle
b. FF1 and FF2 to both latch
c. FF1 to latch; FF2 to toggle
d. FF1 to toggle; FF2 to latch
LOW

## Slide 71
© 2008 Pearson Education
Quiz
6. A 4-bit binary counter has a terminal count of
a. 4
b. 10
c. 15
d. 16

## Slide 72
© 2008 Pearson Education
Quiz
7. Assume the clock for a 4-bit binary counter is 80 kHz. The output frequency of the fourth stage (Q3) is
a. 5 kHz
b. 10 kHz
c. 20 kHz
d. 320 kHz

## Slide 73
8. A 3-bit count sequence is shown for a counter (Q2 is the MSB). The sequence is
a. 0-1-2-3-4-5-6-7-0 (repeat)
b. 0-1-3-2-6-7-5-4-0 (repeat)
c. 0-2-4-6-1-3-5-7-0 (repeat)
d. 0-4-6-2-3-7-5-1-0 (repeat)
© 2008 Pearson Education
Quiz
Q0
Q1
Q2

## Slide 74
9. FF2 represents the MSB. The counts that are being decoded by the 3-input AND gates are
a. 2 and 3
b. 3 and 6
c. 2 and 5
d. 5 and 6
© 2008 Pearson Education
Quiz

## Slide 75
10. Assume the input frequency (fin) is 256 Hz. The output frequency (fout) will be
a. 16 Hz
b. 1 kHz
c. 65 kHz
d. none of the above
© 2008 Pearson Education
Quiz
HIGH
CLK
Q0
Q1
Q2
C
Counter 1
Counter 2
C
CTEN
CTEN
CTR DIV 16
CTR DIV 16
Q3
Q0
Q1
Q2
Q3
TC
TC
fin
fout

## Slide 76
Answers:
1. a
2. d
3. c
4. d
5. b
6. c
7. a
8. b
9. b
10. d
Quiz