## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Chapter 9
© 2008 Pearson Education

## Slide 2
A shift register is an arrangement of flip-flops with important applications in storage and movement of data. Some basic data movements are illustrated here.
Summary
Basic Shift Register Operations
Data in
Data in
Data in
Data in
Data in
Data out
Data out
Data out
Data out
Data out
Serial in/shift right/serial out
Serial in/shift left/serial out
Parallel in/serial out
Parallel in/parallel out
Serial in/parallel out
Rotate right
Rotate left

## Slide 3
Summary
Serial-in/Serial out Shift Register
Shift registers are available in IC form or can be constructed from discrete flip-flops as is shown here with a five-bit serial-in serial-out register.
Each clock pulse will move an input bit to the next flip-flop. For example, a 1 is shown as it moves across.
1
1
1
1
1
1
CLK
CLK
CLK
CLK
CLK

## Slide 4
Summary
An application of shift registers is conversion of serial data to parallel form.
For example, assume the binary number 1011 is loaded sequentially, one bit at each clock pulse.
CLK
CLK
CLK
CLK
After 4 clock pulses, the data is available at the parallel output.
Serial-in/Parallel out Shift Register

## Slide 5
Summary
The 74HC164A Shift Register
The 74HC164A is a CMOS 8-bit serial in/parallel out shift register. VCC can be from +2.0 V to +6.0 V.
One of the two serial data inputs may be used as an active HIGH enable to gate the other input. If no enable is needed, the other serial input can be connected to VCC. The 74HC164A has an active LOW asynchronous clear. Data is entered on the leading-edge of the clock.
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B

## Slide 6
Summary
Waveforms for the 74HC164A
Sample waveforms for the 74HC164A are shown. Notice that B acts as an active HIGH enable for the data on A as discussed.
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B
Outputs
Clear
Clear
As with CMOS devices, unused inputs should always be connected to a logic level; unused outputs should be left open.

## Slide 7
Summary
Parallel in/Serial out Shift Register
Shift registers can be used to convert parallel data to serial form. A logic diagram for this type of register is shown:
D0
D1
D2
D3
Q0
Q1
Q2
Q3
SHIFT/LOAD
CLK
Serial data out

## Slide 8
Summary
The 74HC165 Shift Register
The 74HC165 is a CMOS 8-bit parallel in/serial out shift register. The logic symbol is shown:
D0
D1
D2
D3
D4
D5
D6
D7
Q7
Q7
SH/LD
CLK
SER
CLK INH
The clock (CLK) and clock inhibit (CLK INH) lines are connected to a common OR gate, so either of these inputs can be used as an active-LOW clock enable with the other as the clock input. Data is loaded asynchronously when SH/LD is LOW and moved through the register synchronously when SH/LD is HIGH and a rising clock pulse occurs.

## Slide 9
Summary
The 74HC165 Shift Register
A Multisim simulation of the 74165A is shown. The word generator is used as a source for the pattern shown in the green probes.
MSB
Pattern is loaded when J1 is LOW
Q7 is labeled QH in Multisim

## Slide 10
Summary
The 74HC165 Shift Register
Here the scope is opened and you can observe the pattern. The MSB is HIGH and is on the Q7 output as soon as LOAD is LOW.
Load
Q7
Clk
MSB

## Slide 11
Summary
Bidirectional Shift Register
Bidirectional shift registers can shift the data in either direction using a RIGHT/LEFT input.
HIGH on the RIGHT / LEFT control input allows data bits inside the register to be shifted to the right, LOW enables bits inside the register to be shifted to the left.
R/L=1, gates G1-G4 enabled
R/L=0, gates G5-G8 enabled

## Slide 12
Summary
Bidirectional Shift Register
The animation performs right shift four times, then left shift four times. Notice the order of the four output bits are not the same as the order of the original four input bits. They are actually reversed!

## Slide 13
Summary
Bidirectional Shift Register
CLK
RIGHT/LEFT
Serial data in
Q0
Q1
Q2
Q3
Shift right
Shift left
Question
How will the pattern change if the RIGHT/LEFT control signal is inverted?
Answer
See display
Shift right
Shift left

## Slide 14
Summary
Universal Shift Register
A universal shift register has both serial and parallel input and output capability. The 74HC194 is an example of a 4-bit bidirectional universal shift register.
D0
D1
D2
D3
CLK
SL SER
Q0
Q1
Q2
Q3
SR SER
S1
S0
CLR
Sample waveforms are on the following slide…

## Slide 15
Summary
Universal Shift Register

## Slide 16
Summary
Shift Register Counters
Shift registers can form useful counters by recirculating a pattern of 0s and 1s.
Ring Counters
Straight
Overbeckcounter or Ring counter
Twisted
JohnsonorMoebiuscounter
Hamming Distance = 2
1000, 0100, 0010, 0001, 1000... .
Hamming Distance = 1
0000, 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000... .
Both the Ring and the Johnson counter must initially be forced into a valid state in the count sequence because they operate on a subset of the available number of states.
MOD = n
MOD = 2n

## Slide 17
Summary
Straight Ring Counter
A straight ring counter or Overbeck counter connects the output of the last FF in the shift register to the first FF of the shift register input and circulates a single one (or zero) bit around the ring.
In a 4-register one-hot counter, with initial register values of 1000, the repeating pattern is: 1000, 0100, 0010, 0001, 1000... .
One of the registers must be pre-loaded with a 1 (or 0) in order to operate properly.

## Slide 18
Summary
(Straight) Ring Counter
The ring counter can be implemented with either D flip-flops or J-K flip-flops.
Here is a 4-bit ring counter constructed from a series of D flip-flops. Notice the feedback.
It can also be implemented with J-K flip flops.

## Slide 19
Summary
Ring Counter
Redrawing the Ring counter (without the clock shown) shows why it is a “ring”.
The disadvantage to this counter is that it must be preloaded with the desired pattern (usually a single 0 or 1) and it has even fewer states than a Johnson counter (n, where n = number of flip-flops.

## Slide 20
Summary
Ring Counter
A common pattern for a ring counter is to load it with a single 1 or a single 0. The waveforms shown here are for an 8-bit ring counter with a single 1.

## Slide 21
Summary
4-bit Ring Counter
Only 4 of the maximum 16 states are used, making ring counters very inefficient in terms of state usage.

## Slide 22
Summary
Twisted Ring Counter
A twisted ring counter, also called Johnson counter or Moebius counter, connects the complement of the output of the last shift register to the input of the first register and circulates a stream of ones followed by zeros around the ring.
For example, in a 4-register counter, with initial register values of 0000, the repeating pattern is: 0000, 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000... .

## Slide 23
Summary
Shift Register Counters
The Johnson counter can be made with a series of D flip-flops
… or with a series of J-K flip flops. Here Q3 and Q3 are fed-back to the J0 and K0 inputs with a “twist”.

## Slide 24
Summary
Johnson Counter
“twist”
Redrawing the same Johnson counter (without the clock shown) illustrates why it is sometimes called as a “twisted-ring” counter.

## Slide 25
Summary
Moebius Counter – The Name

## Slide 26
Summary
Johnson Counter
The Johnson counter is useful when you need a sequence that changes by only one bit at a time but it has a limited number of states (2n, where n = number of stages).
The first five counts for a 4-bit Johnson counter that is initially cleared are: CLK Q0 Q1 Q2 Q3
0 0 0 0
1 0 0 0
1 1 0 0
1 1 1 0
1 1 1 1
0 1 1 1
0 0 1 1
0 0 0 1
0
1
2
3
4
5
6
7
What are the remaining 3 states?
Question

## Slide 27
Summary
4-bit Johnson Counter
Disadvantage of this counter is that the maximum
available states are not fully utilized.
Only eight of the sixteen states are being used.

## Slide 28
Summary
Shift Register Applications
Shift registers can be used to delay a digital signal by a predetermined amount.
Example
An 8-bit serial in/serial out shift register has a 40 MHz clock. What is the total delay through the register?
Solution
The delay for each clock is 1/40 MHz = 25 ns
The total delay is 8 x 25 ns = 200 ns
25 ns
= 200 ns

## Slide 29
Summary
Shift Register Applications
A UART (Universal Asynchronous Receiver Transmitter) is a serial-to-parallel converter and a parallel to serial converter.
UARTs are commonly used in small systems where one device must communicate with another. Parallel data is converted to asynchronous serial form and transmitted. The serial data format is:
Start
Bit (0)
Stop Bits (1)
Data bus
Serial data in
Serial data out
CLK
CLK

## Slide 30
Summary
Keyboard Encoder
The keyboard encoder is an example of where a ring counter is used in a small system to encode a key press.
Two 74HC195 shift registers are connected as an 8-bit ring counter preloaded with a single 0. As the 0 circulate in the ring counter, it “scans” the keyboard looking for any row that has a key closure. When one is found, a corresponding column line is connected to that row line. The combination of the unique column and row lines identifies the key. The schematic is shown on the following slide…

## Slide 31
© 2008 Pearson Education

## Slide 32
Key Terms
Register
Stage
Shift
Load
Bidirectional
One or more flip-flops used to store and shift data.
One storage element in a register.
To move binary data from stage to stage within a shift register or other storage device or to move binary data into or out of the device.
To enter data in a shift register.
Having two directions. In a bidirectional shift register, the stored data can be shifted right or left.

## Slide 33
1. The shift register that would be used to delay serial data by
4 clock periods is
a. c.
b. d.
© 2008 Pearson Education
Quiz

## Slide 34
© 2008 Pearson Education
Quiz
2. The circuit shown is a
a. serial-in/serial-out shift register
b. serial-in/parallel-out shift register
c. parallel-in/serial-out shift register
d. parallel-in/parallel-out shift register

## Slide 35
Quiz
3. If the SHIFT/LOAD line is HIGH, data
a. is loaded from D0, D1, D2 and D3 immediately
b. is loaded from D0, D1, D2 and D3 on the next CLK
c. shifted from left to right on the next CLK
d. shifted from right to left on the next CLK
© 2008 Pearson Education

## Slide 36
© 2008 Pearson Education
Quiz
4. A 4-bit parallel-in/parallel-out shift register will store data for
a. 1 clock period
b. 2 clock periods
c. 3 clock periods
d. 4 clock periods

## Slide 37
5. The 74HC164 (shown) has two serial inputs. If data is placed on the A input, the B input
a. could serve as an active LOW enable
b. could serve as an active HIGH enable
c. should be connected to ground
d. should be left open
© 2008 Pearson Education
Quiz
CLK
Q0
Q1
Q2
Q3
CLR
Q4
Q5
Q6
Q7
Serial inputs
A
B

## Slide 38
Quiz
6. An advantage of a ring counter over a Johnson counter is that the ring counter
a. has more possible states for a given number of flip-flops
b. is cleared after each cycle
c. allows only one bit to change at a time
d. is self-decoding

## Slide 39
Quiz
7. A possible sequence for a 4-bit ring counter is
a. … 1111, 1110, 1101 …
b. … 0000, 0001, 0010 …
c. … 0001, 0011, 0111 …
d. … 1000, 0100, 0010 …

## Slide 40
Quiz
8. The circuit shown is a
a. serial-in/parallel-out shift register
b. serial-in/serial-out shift register
c. ring counter
d. Johnson counter

## Slide 41
9. Assume serial data is applied to the 8-bit shift register
shown. The clock frequency is 20 MHz. The first data bit
will show up at the output in
a. 50 ns
b. 200 ns
c. 400 ns
d. 800 ns
© 2008 Pearson Education
Quiz

## Slide 42
10. For transmission, data from a UART is sent in
a. asynchronous serial form
b. synchronous parallel form
c. can be either of the above
d. none of the above
© 2008 Pearson Education
Quiz

## Slide 43
Answers:
1. a
2. c
3. c
4. a
5. b
6. d
7. d
8. d
9. c
10. a
Quiz