## Slide 1: Memory
Memory Organization, hierarchy, RAM, ROM, Memory Address map, Cache, Memory Management

## Slide 2: Key Characteristics of Computer Memory Systems
Table 4.1 Key Characteristics of Computer Memory Systems

## Slide 3: Characteristics of Memory Systems
Location
  Refers to whether memory is internal and external to the computer
  Internal memory is often equated with main memory
  Processor requires its own local memory, in the form of registers
  Cache is another form of internal memory
  External memory consists of peripheral storage devices that are accessible to the processor via I/O controllers
Capacity
  Memory is typically expressed in terms of bytes (1 byte=8 bits or words)
  Common word lengths are 8, 16, and 32 bits.
Unit of transfer
  For internal memory the unit of transfer is equal to the number of electrical lines into and out of the memory module
  This may be equal to the word length, but is often larger, such as 64, 128, or 256 bits.

## Slide 6: Memory
  The most common forms are:
  Semiconductor memory
  Magnetic surface memory
  Optical
  Magneto-optical
  Several physical characteristics of data storage are important:
  Volatile memory
    Information decays naturally or is lost when electrical power is switched off
  Nonvolatile memory
    Once recorded, information remains without deterioration until deliberately changed
    No electrical power is needed to retain information
  Magnetic-surface memories
    Are nonvolatile
  Semiconductor memory
    May be either volatile or nonvolatile
  Nonerasable memory
    Cannot be altered, except by destroying the storage unit
    Semiconductor memory of this type is known as read-only memory (ROM)
  For random-access memory the organization is a key design issue
  Organization refers to the physical arrangement of bits to form words

## Slide 7: Memory Hierarchy
Design constraints on a computer’s memory can be summed up by three questions:
  How much, how fast, how expensive
There is a trade-off among capacity, access time, and cost
  Faster access time, greater cost per bit
  Greater capacity, smaller cost per bit
  Greater capacity, slower access time
The way out of the memory dilemma is not to rely on a single memory component or technology, but to employ a memory hierarchy

## Slide 8: Memory Hierarchy - Diagram
As one goes down the hierarchy, the following occur:
a. Decreasing cost per bit
b. Increasing capacity
c. Increasing access time
d. Decreasing frequency of access of the memory by the processor

## Slide 9: Internal Memory
ROM, DRAM, and SRAM

## Slide 10: Memory Cell Operation

## Slide 11: Semiconductor Memory Types
Table 5.1 Semiconductor Memory Types

## Slide 12: Dynamic RAM (DRAM)
RAM technology is divided into two technologies:
  Dynamic RAM (DRAM)
  Static RAM (SRAM)
  DRAM
    Made with cells that store data as charge on capacitors
    Presence or absence of charge in a capacitor is interpreted as a binary 1 or 0
    Requires periodic charge refreshing to maintain data storage
    The term dynamic refers to tendency of the stored charge to leak away, even with power continuously applied

## Slide 13: Static RAM (SRAM)
  Digital device that uses the same logic elements used in the processor
  Binary values are stored using traditional flip-flop logic gate configurations
  Will hold its data as long as power is supplied to it

## Slide 14: SRAM versus DRAM
Both volatile
  Power must be continuously supplied to the memory to preserve the bit values
Dynamic cell
  Simpler to build, smaller
  More dense (smaller cells = more cells per unit area)
  Less expensive
  Requires the supporting refresh circuitry
  Tend to be favored for large memory requirements
  Used for main memory
Static
  Faster
  Used for cache memory (both on and off chip)
SRAM
DRAM

## Slide 15: Read Only Memory (ROM)
Contains a permanent pattern of data that cannot be changed or added to
No power source is required to maintain the bit values in memory
Data or program is permanently in main memory and never needs to be loaded from a secondary storage device
Data is actually wired into the chip as part of the fabrication process
  Disadvantages of this:
    No room for error, if one bit is wrong the whole batch of ROMs must be thrown out
    Data insertion step includes a relatively large fixed cost

## Slide 16: Programmable ROM (PROM)
Less expensive alternative
Nonvolatile and may be written into only once
Writing process is performed electrically and may be performed by supplier or customer at a time later than the original chip fabrication
Special equipment is required for the writing process
Provides flexibility and convenience
Attractive for high volume production runs

## Slide 17: Read-Mostly Memory
EPROM
Erasable programmable read-only memory
Erasure process can be performed repeatedly
More expensive than PROM but it has the advantage of the multiple update capability
EEPROM
Electrically erasable programmable read-only memory
Can be written into at any time without erasing prior contents
Combines the advantage of non-volatility with the flexibility of being updatable in place
More expensive than EPROM
Flash Memory
Intermediate between EPROM and EEPROM in both cost and functionality
Uses an electrical erasing technology, does not provide byte-level erasure
Microchip is organized so that a section of memory cells are erased in a single action or “flash”

## Slide 18: Typical 16 Mb DRAM (4M x 4)
RAS= Row Address Select
CAS= Column Address Select
WE= Write Enable
OE= Output Enable

## Slide 19: Chip Packaging
The power supply to the chip (Vcc).
A ground pin (Vss).
A program voltage (Vpp) that is supplied during programming (write operations).

## Slide 20: Error Correction
Hard Failure
  Permanent physical defect
  Memory cell or cells affected cannot reliably store data but become stuck at 0 or 1 or switch erratically between 0 and 1
  Can be caused by:
    Harsh environmental abuse
    Manufacturing defects
Soft Error
  Random, non-destructive event that alters the contents of one or more memory cells
  No permanent damage to memory
  Can be caused by:
    Power supply problems
    Alpha particles due to radioactivity falloff which is common in all materials

## Slide 21: Advanced DRAM Organization
  One of the most critical system bottlenecks when using high-performance processors is the interface to main internal memory
  The traditional DRAM chip is constrained both by its internal architecture and by its interface to the processor’s memory bus
  A number of enhancements to the basic DRAM architecture have been explored:
Table 5.3 Performance Comparison of Some DRAM Alternatives
Synchronous SDRAM
RamBus
RDRAM
Double Data Rate
DDR-DRAM

## Slide 22: Synchronous DRAM (SDRAM)
One of the most widely used forms of DRAM
Exchanges data with the processor synchronized to an external clock signal and running at the full speed of the processor/memory bus without imposing wait states
With synchronous access the DRAM moves data in and out under control of the system clock
The processor or other master issues the instruction and address information which is latched by the DRAM
The DRAM then responds after a set number of clock cycles
Meanwhile the master can safely do other tasks while the SDRAM is processing

## Slide 23: RDRAM
Developed by Rambus
Adopted by Intel for its Pentium and Itanium processors
Has become the main competitor to SDRAM
Chips are vertical packages with all pins on one side
Exchanges data with the processor over 28 wires no more than 12 centimeters long
Bus delivers address and control information using an asynchronous block-oriented protocol
Gets a memory request over the high-speed bus
Request contains the desired address, the type of operation, and the number of bytes in the operation

## Slide 24: Double Data Rate SDRAM (DDR SDRAM)
SDRAM can only send data once per bus clock cycle
Double-data-rate SDRAM can send data twice per clock cycle, once on the rising edge of the clock pulse and once on the falling edge

## Slide 25: Cache Memory
Cache memory is designed to combine the memory access time of expensive, high-speed memory combined with the large memory size of less expensive, lower-speed memory.

## Slide 26: Cache and Main Memory

## Slide 27
Suppose that the processor has access to two levels of memory. Level 1contains 1000 words and has an access time of 0.01 s; level 2 contains 100,000 words and has an access time of 0.1 µs. Assume that if a word to be accessed is in level 1, then the processor accesses it directly. If it is in level 2, then the word is first transferred to level 1 and then accessed by the processor. For simplicity, we ignore the time required for the processor to determine whether the word is in level 1 or level 2.
Suppose 95% of the memory accesses are found in the cache. Then the average time to access a word can be expressed as
(0.95)(0.01 µs) + (0.05)(0.01 µs + 0.1 µs) = 0.0095 + 0.0055 = 0.015 µs
The average access time is much closer to 0.01 µs than to 0.1 µs, as desired.
Cache and Main Memory

## Slide 28: Cache/Main Memory Structure

## Slide 29: Elements of Cache Design
Table 4.2 Elements of Cache Design

## Slide 30: Logical and Physical Caches

## Slide 31: Cache Addresses
Virtual memory
  Facility that allows programs to address memory from a logical point of view, without regard to the amount of main memory physically available
  When used, the address fields of machine instructions contain virtual addresses
  For reads to and writes from main memory, a hardware memory management unit (MMU) translates each virtual address into a physical address in main memory
Virtual Memory

## Slide 32: Magnetic Disk
A disk is a circular platter constructed of nonmagnetic material, called the substrate, coated with a magnetizable material
  Traditionally the substrate has been an aluminium or aluminium alloy material
  Recently glass substrates have been introduced
Benefits of the glass substrate:
  Improvement in the uniformity of the magnetic film surface to increase disk reliability
  A significant reduction in overall surface defects to help reduce read-write errors
  Ability to support lower fly heights
  Better stiffness to reduce disk dynamics
  Greater ability to withstand shock and damage

## Slide 33: Disk Data Layout

## Slide 34: Disk Layout Methods Diagram