## Slide 1: Computer Organization and Architecture Week 4

## Slide 2: Clock Speed and Instructions Per Second
Operations performed by a processor, such as fetching an instruction, decoding the instruction, performing an arithmetic operation, and so on, are governed by a system clock.
Typically, all operations begin with the pulse of the clock. Thus, at the most fundamental level, the speed of a processor is dictated by the pulse frequency produced by the clock, measured in cycles per second, or Hertz (Hz).
Notes: .

## Slide 3: Common Prefixed Units / Frequency
Value | Symbol | Name | Amount
102 | Hz | hertz | cycles per second
103 Hz | kHz | kilohertz | 1,000
106 Hz | MHz | megahertz | 1,000,000
109 Hz | GHz | gigahertz | 1,000,000,000
1012 Hz | THz | Terahertz | 1,000,000,000,000
1015 Hz | PHz | petahertz | 1,000,000,000,000,000

## Slide 4: System Clock
Typically, clock signals are generated by a quartz crystal, which generates a constant signal wave while power is applied. This wave is converted into a digital voltage pulse stream that is provided in a constant flow to the processor circuitry

## Slide 5: System Clock
For example, a 1-GHz processor receives 1 billion pulses per second.
The rate of pulses is known as the clock rate, or clock speed. One increment, or pulse, of the clock is referred to as a clock cycle, or a clock tick. The time between pulses is the cycle time.

## Slide 6: System Clock
The execution of an instruction involves a number of discrete steps, such as fetching the instruction from memory, decoding the various portions of the instruction, loading and storing data, and performing arithmetic and logical operations.
Thus, most instructions on most processors require multiple clock cycles to complete. Some instructions may take only a few cycles, while others require dozens.

## Slide 7: Terminologies

## Slide 8: Cycles Per Instruction (CPI)
Suppose there are 3 types of instructions e.g. Addition, Subtraction and Multiplication.
CPIi be the number of cycles required for instruction type i
Ii be the number of executed instructions of type i for given program

## Slide 9: Cycles Per Instruction (CPI)

## Slide 10: Average Cycles Per Instruction (CPI)

## Slide 11
Measurement
10-3 Millie Sec
10-6 Micro Sec
10-9 Nano Sec
10-12 Pico Sec

## Slide 12: Five Performance Factors are influenced by Four System Attributes
p =Number of processors
m =Number of memory references
k = ratio between memory cycle time and processor cycle time
A common measure of performance for a processor is the rate at which instructions are executed, expressed as millions of instructions per second (MIPS), referred to as the MIPS rate.

## Slide 13: MIPS (Millions of Instructions Per Second)

## Slide 14: MIPS (Millions of Instructions Per Second)

## Slide 15: MIPS (Millions of Instructions Per Second)

## Slide 16: Another Example
Instruction Type | CPI | Instruction Mix (%)
Arithmetic and Logic | 1 | 60
Load/store with cache hit | 2 | 18
Branch | 4 | 12
Memory reference with cache miss | 8 | 10
Consider the execution of a program that results in the execution of 2 million instructions on a 400-MHz processor. The Instruction types are given below.

## Slide 17: Exercise
Instruction Type | Instruction Count | Cycles per Instructions
Integer Arithmetic | 45000 | 1
Data Transfer | 32000 | 2
Floating Point | 15000 | 2
Control Transfer | 8000 | 2
A program is run on a 40 MHz Processor.
Determine the CPI and MIPS rate

## Slide 18: Benchmarks
For example, consider this high-level language statement:
A = B + C /* assume all quantities in main memory */
With a traditional instruction set architecture, referred to as a complex instruction set computer (CISC), this instruction can be compiled into one processor instruction:
add mem(B), mem(C), mem (A)
On a typical RISC machine, the compilation would look something like this:
load mem(B), reg(1);
load mem(C), reg(2);
add reg(1), reg(2), reg(3);
store reg(3), mem (A)